#### 09 - Engine, 6.2L/Lubrication/OIL/Standard Procedure

## STANDARD PROCEDURE - ENGINE OIL SERVICE

### CRANKCASE OIL LEVEL INSPECTION

The oil level indicator is located on the right side of the engine.

| CAUTION: | Do not overfill crankcase with engine oil, pressure loss or oil foaming can result. |
| --- | --- |

Inspect the engine oil level approximately every 800 kilometers (500 miles). Unless the engine has exhibited loss of oil pressure, run the engine for about ten minutes before checking the oil level. Checking the engine oil level on a cold engine is not accurate.

To ensure proper lubrication of an engine, the engine oil must be maintained at an acceptable level. The acceptable levels are indicated between the ADD and SAFE marks on the engine oil level indicator.

- Position the vehicle on the level surface.

- With the engine off, allow approximately five minutes for the oil to settle to the bottom of the crankcase and then remove the engine oil level indicator.

- Wipe the oil level indicator clean.

- Install the oil level indicator and verify it is seated in the tube.

- Remove the oil level indicator, with the handle held above the tip, observe the oil level reading.

- Add oil only if the level is below the ADD mark on the oil level indicator.

### ENGINE OIL CHANGE

Change the engine oil at the mileage and time intervals described in the Maintenance Schedules (Refer to 04 - Vehicle Quick Reference/Maintenance Schedules - Description) .

- Run the engine until it reaches normal operating temperature, then shut off the engine.

- Remove the oil fill cap.

- Raise and support the vehicle (Refer to 04 - Vehicle Quick Reference/Hoisting/Standard Procedure) .

- Remove the belly pan (Refer to 13 - Frame and Bumpers/Under Body Protection/BELLY PAN - Removal) .

- Place a suitable drain pan under the oil pan drain.

- Remove the drain plug (1) from the oil pan and allow the oil to drain.

- Remove the oil filter (2).

- Place a suitable drain pan under the engine oil cooler.

- Remove the drain plug (1) from the engine oil cooler and allow the oil to drain.

| NOTE: | Allow oil to drain until there is only one drip every second, approximately five minutes. |
| --- | --- |

- Lightly lubricate the NEW oil filter gasket with clean engine oil.

- Fill the NEW oil filter with fresh engine oil.

- Thread the oil filter onto the oil filter adapter.

| NOTE: | Do not over tighten the oil filter. |
| --- | --- |

- When the oil filter gasket makes contact with the oil filter adapter sealing surface, hand tighten the oil filter one half turn, or 180°.

- Clean any residual oil that may have dripped onto the oil cooler hoses (3,4).

- Inspect the drain plug threads for stretching or other damage and replace if necessary.

- Install both drain plugs and tighten to the proper (Torque Specifications) .

- Install the belly pan (Refer to 13 - Frame and Bumpers/Under Body Protection/BELLY PAN - Installation) .

- Lower the vehicle and fill the crankcase with the specified type and amount of engine oil (Refer to 04 - Vehicle Quick Reference/Capacities and Recommended Fluids/Specifications) .

- Install the oil fill cap.

- Start the engine and check for leaks.

- Stop the engine and after five minutes, check the oil level.

| NOTE: | Care should be exercised when disposing of used engine oil. |
| --- | --- |